Separation and Determination of Benzene, Toluene, Ethylbenzene and O-Xylene Compounds in Water Using Directly Suspended Droplet Microextraction coupled with Gas Chromatography-Flame Ionization Detector

A. Sarafraz-Yazdi*1,3, A. H. Amiri 1 ,  Z. Es’haghi 2,3,

1) Department of Chemistry, Faculty of Sciences, Ferdowsi University of Mashhad, Iran

2) Department of Chemistry, Faculty of Sciences, Payame Noor University, Iran

3) Biotechnology Research Center of Ferdowsi University, Mashhad, Iran

Abstract

Directly suspended droplet microextraction technique (DSDME) coupled with GC–FID was used to determine BTEX compounds in aqueous samples. The effective parameters were optimized. The performance of the proposed technique was evaluated for the determination of BTEX compounds in natural water samples. Under the optimal conditions the enrichment factors ranged from 142.68 to 312.13, linear range; 0.01–20 µg L-1, limits of detection; 0.0008–0.010 µg L-1 for most of analytes. Relative standard deviations for 2 µg L-1 of BTEX in water were in the range 1.81–2.47% (n = 5). The recoveries of BTEX from surface water at spiking level of 5.0 µg L-1 were 89.87– 98.62%.

Keywords: Directly suspended droplet microextraction technique (DSDME), BTEX, Water sample, GC-FID.